## Slide 1
ROBUST AUTONOMOUS DRIVING
Evaluating Vision Robustness Under
Real-World Image Distortions
Lane Detection • Feature Matching • Vehicle Detection
Amit Ashkenazi
amit17ashkenazi@gmail.com
Alon Kenan
alon.kenan.ee@gmail.com

## Slide 2
PROJECT OVERVIEW
Why Robustness Matters
Classical computer-vision and deep-learning methods used in autonomous driving are normally evaluated on clean images. On the road, cameras see low light, motion blur, and rain every day.
This project measures how much performance each method loses as distortion severity increases — and how much of it can be recovered.
1
Measure degradation
Sweep 3 realistic distortions across 9 severity levels, scored vs. achieved SNR.
2
Enhancement recovery
Restore the image first (denoise / deblur / de-rain), then re-run the same method.
3
Fine-tuning recovery
Adapt the model itself to distorted inputs, using real ground truth.
Robust Autonomous Driving Under Image Distortions
2

## Slide 3
THE DATASET
BDD100K — Real Driving Scenes
Berkeley DeepDrive: large-scale, diverse road-scene images/video with object, lane, and drivable-area annotations — the source for all three tasks.
Dataset 1 — 300 images → Task 1 (Lane Detection) & Task 3 (Vehicle Detection)
Dataset 2 — 178 consecutive-frame pairs from one driving video → Task 2 (Feature Matching)
Robust Autonomous Driving Under Image Distortions
3

## Slide 4
THREE TASKS, THREE LEVELS OF VISION
One Pipeline, Three Perception Methods
Task 1
Lane Detection
Canny + Hough Transform
Classical — Low Level
Task 2
Feature Matching
ORB + BFMatcher + RANSAC
Classical — High Level
Task 3
Vehicle Detection
YOLOv8n
Deep Learning
Robust Autonomous Driving Under Image Distortions
4

## Slide 5
TASK 1
Lane Detection
Grayscale + blur → Canny edges → trapezoidal ROI mask → morphological closing → probabilistic Hough transform → slope filtering → outlier rejection → weighted regression per side.
Identifies the ego-vehicle's lane boundaries — a core low-level building block for lane-keeping and path planning.
Clean-image result
Robust Autonomous Driving Under Image Distortions
5

## Slide 6
TASK 2
Feature Matching
ORB keypoint detection → BFMatcher (Hamming distance) k-NN → Lowe's ratio test → RANSAC homography, keeping only geometrically consistent inlier matches.
Building block behind visual odometry and tracking — matched between two consecutive frames of the same driving sequence, mimicking real frame-to-frame matching.
Clean-image match visualization — two consecutive frames
Robust Autonomous Driving Under Image Distortions
6

## Slide 7
TASK 3
Vehicle Detection
YOLOv8n (nano) — pretrained on COCO, later fine-tuned on distorted driving images. Locates and classifies car / truck / bus / motorcycle / bicycle.
★ The only task with real BDD100K ground truth — unlike Tasks 1 & 2, which use pseudo-GT (clean-image output as reference).
Clean-image detection result
Robust Autonomous Driving Under Image Distortions
7

## Slide 8
EVALUATION
One Headline Metric per Task
Chosen for actually telling a robustness story — monotonic with severity, not flat or noisy.
Task 1
survival_rate
Lane line neither lost nor displaced >45px vs. clean-image reference
1.00
clean baseline
Task 2
match_ratio_vs_baseline
Match coverage relative to the clean-baseline's fixed keypoint budget
0.083
mean, 178 pairs
Task 3
matched_recall
Fraction of real GT boxes found (class-aware IoU ≥ 0.5)
0.366
mean, 300 images, vs. real GT
Robust Autonomous Driving Under Image Distortions
8

## Slide 9
SIMULATED REAL-WORLD CONDITIONS
Three Distortions × Nine Severity Levels
Each swept mild → extreme, scored against achieved SNR (dB).
Low Light
Dusk / night / tunnel driving — brightness + gamma darkening.
Motion Blur
Camera/vehicle motion during exposure — linear blur kernel.
Rain
Rain-streak occlusion — adds clutter, keeps scene structure.
Robust Autonomous Driving Under Image Distortions
9

## Slide 10
UNDER DISTORTION
Robustness Falls — At Different Rates
Metric vs. SNR for each task, all three distortions overlaid.
Task 1 — survival_rate
Task 2 — match_ratio_vs_baseline
Task 3 — matched_recall
Task 1: low_light/motion_blur collapse at extreme severity; rain degrades gently. Task 2: monotonic decline, sharpest for blur/darkness. Task 3: recall drops monotonically; low_light hurts most.
Robust Autonomous Driving Under Image Distortions
10

## Slide 11
RECOVERY STRATEGY 1
Image Enhancement
Fixed pre-processing restoration, applied before re-running each method.
Low Light Gamma lift + CLAHE (LAB L-channel)
Motion Blur Unsharp masking
Rain Edge-preserving bilateral filter
Task 1 — clean vs. distorted vs. enhanced
Task 2 — clean vs. distorted vs. enhanced
Task 3 — clean vs. distorted vs. enhanced
Enhancement helps unevenly: Task 1's low_light/motion_blur improve but rain slightly worsens (de-rain filter smooths the thin edges Hough needs); Task 2 improves for motion_blur/rain; Task 3 improves for low_light/rain, flat for motion_blur.
Robust Autonomous Driving Under Image Distortions
11

## Slide 12
RECOVERY STRATEGY 2
Fine-Tuning YOLOv8n
Adapting the model's weights to the distorted domain, using real ground truth.
Mean recall across all 9 levels
distorted
enhanced
fine-tuned
low_light
0.262
0.355
0.414
motion_blur
0.259
0.261
0.451
rain
0.260
0.275
0.452
Fine-tuning wins on all 3 distortions — the gap over enhancement is largest exactly where enhancement helped least (motion_blur, rain).
Robust Autonomous Driving Under Image Distortions
12

## Slide 13
TRANSPARENCY
Known Issues & Limitations
Pseudo-GT for Tasks 1 & 2
BDD100K's lane-marking and fine-grained-matching label releases weren't locally available; clean-image output serves as the reference instead of human-labeled GT.
Dataset pruning
Task 3 narrowed 675→300 images to match Task 1 and guarantee 100% real-GT coverage; this subset has zero motorcycle/bicycle instances. 105 source images were found corrupt and replaced before any results were produced.
CPU-only fine-tuning
15 epochs, 240 training images, one fixed severity/distortion each — a larger, more varied set and GPU training would likely improve results further.
SNR as a proxy
A uniform-noise measure that doesn't perfectly reflect perceptual severity for structured distortions like rain.
Robust Autonomous Driving Under Image Distortions
13

## Slide 14
Key Takeaway
Enhancement recovers some performance;
fine-tuning recovers more.
Every task degrades under real-world distortion — the two recovery strategies are complementary, not interchangeable: enhancement is cheap and model-agnostic, fine-tuning adapts the model itself and wins when the domain shift is large.
Thank you